Solution
# 1. Network Topology Design

Server Room (3rd Floor – IT Department)
There will be 3 routers connected with serial cables (triangle)

        R1
       / \
   R2 ------ R3

Router purpose:
Router	Floor	Departments
R1	1st Floor	Reception, Store, Logistics
R2	2nd Floor	Finance, HR, Sales
R3	3rd Floor	IT, Admin

Each floor has:
- 1 Switch
- 1 Wireless Router / Access Point
- Department PCs
- 1 Printer per department
# 2. Router-to-Router Networks (/30)

Link	Network
R1 – R2	10.10.10.0/30
R2 – R3	10.10.10.4/30
R1 – R3	10.10.10.8/30

Example:
Interface	IP
R1 S0/0/0	10.10.10.1
R2 S0/0/0	10.10.10.2

R2 S0/0/1 | 10.10.10.5 |
R3 S0/0/0 | 10.10.10.6 |
R1 S0/0/1 | 10.10.10.9 |
R3 S0/0/1 | 10.10.10.10 |
# 3. VLAN & Subnet Design
### 1st Floor
Department	VLAN	Network
Reception	VLAN 80	192.168.80.0/24
Store	VLAN 70	192.168.70.0/24
Logistics	VLAN 60	192.168.60.0/24

### 2nd Floor
Department	VLAN	Network
Finance	VLAN 50	192.168.5.0/24
HR	VLAN 40	192.168.4.0/24
Sales	VLAN 30	192.168.3.0/24

### 3rd Floor
Department	VLAN	Network
Admin	VLAN 20	192.168.2.0/24
IT	VLAN 10	192.168.1.0/24

# 4. Switch VLAN Configuration (Example Floor 1)

enable
configure terminal
vlan 80
name RECEPTION
vlan 70
name STORE
vlan 60
name LOGISTICS

Assign ports:

interface fa0/1
switchport mode access
switchport access vlan 80
interface fa0/2
switchport mode access
switchport access vlan 70
interface fa0/3
switchport mode access
switchport access vlan 60

Trunk to router:

interface fa0/24
switchport mode trunk
# 5. Router-on-a-Stick (Example Router R1)

enable
conf t
interface g0/0
no shutdown
### Reception

interface g0/0.80
encapsulation dot1Q 80
ip address 192.168.80.1 255.255.255.0
### Store

interface g0/0.70
encapsulation dot1Q 70
ip address 192.168.70.1 255.255.255.0
### Logistics

interface g0/0.60
encapsulation dot1Q 60
ip address 192.168.60.1 255.255.255.0
# 6. Serial Interface Configuration

Example R1

interface s0/0/0
ip address 10.10.10.1 255.255.255.252
clock rate 64000
no shutdown
interface s0/0/1
ip address 10.10.10.9 255.255.255.252
clock rate 64000
no shutdown
# 7. OSPF Routing (All Routers)

router ospf 1
network 10.10.10.0 0.0.0.15 area 0
network 192.168.0.0 0.0.255.255 area 0
# 8. DHCP Configuration (Example R1)

Exclude router IP

ip dhcp excluded-address 192.168.80.1
ip dhcp excluded-address 192.168.70.1
ip dhcp excluded-address 192.168.60.1

Reception DHCP

ip dhcp pool RECEPTION
network 192.168.80.0 255.255.255.0
default-router 192.168.80.1
dns-server 8.8.8.8

Store DHCP

ip dhcp pool STORE
network 192.168.70.0 255.255.255.0
default-router 192.168.70.1
dns-server 8.8.8.8

Logistics DHCP

ip dhcp pool LOGISTICS
network 192.168.60.0 255.255.255.0
default-router 192.168.60.1
dns-server 8.8.8.8
# 9. SSH Configuration (All Routers)

hostname R1
ip domain-name hotel.com
crypto key generate rsa
1024
username admin secret cisco
line vty 0 4
login local
transport input ssh
ip ssh version 2

# 10. Port Security (Important Part)
Switch in IT department.
Test PC connected to Fa0/1

interface fa0/1
switchport mode access
switchport port-security
switchport port-security maximum 1
switchport port-security mac-address sticky
switchport port-security violation shutdown

# 11. Test PC Setup
Test PC connected to:

Switch IT
Fa0/1

Use this PC to test SSH
Example command:

ssh -l admin 192.168.1.1
# 12. Wireless Network
Connect Access Point to Switch
Configure:
SSID:
HotelWiFi_Floor1
HotelWiFi_Floor2
HotelWiFi_Floor3

Use WPA2 password
Connect:
- Laptops
- Phones
They will receive DHCP IP automatically
# 13. Printer Setup

Each department:
1 printer
Example:
Reception Printer
IP: DHCP
VLAN 80

# 14. Testing
Verify:
### DHCP
ipconfig
### OSPF
show ip route
### Router connectivity
ping 192.168.3.10
### SSH
ssh -l admin 192.168.1.1
# 15. Final Expected Result
✔ VLAN segmentation
✔ Inter-VLAN routing
✔ OSPF routing
✔ DHCP automatic IP assignment
✔ Wireless access
✔ SSH remote management
✔ Port security protection
✔ All floors communicate