Vic Modern Hotel Network Design Case Study
## Overview
As part of an end-year networking project, the objective is to design and implement a network infrastructure for Vic Modern Hotel.
The hotel consists of three floors, each containing different departments:
- 1st Floor: Reception, Store, Logistics
- 2nd Floor: Finance, HR, Sales/Marketing
- 3rd Floor: IT, Admin
## Design Requirements
### 1. Router Configuration
- A total of three routers must be used.
- Each router represents one floor.
- All routers are placed in the server room (IT Department).
### 2. Router Interconnection
- Routers must be connected using Serial DCE cables.
- The inter-router networks must use the following /30 subnets:
  - 10.10.10.0/30
  - 10.10.10.4/30
  - 10.10.10.8/30
### 3. Switch Deployment
- Each floor must have one switch.
- Switches are placed on their respective floors.
### 4. Wireless Network
- Each floor must provide Wi-Fi connectivity.
- Wireless networks should support:
  - Laptops
  - Mobile devices
### 5. Printers
- Each department must have one printer.
- Printers should be connected to their respective VLANs.
## VLAN and IP Addressing Scheme
### 1st Floor

Department	VLAN ID	Network
Reception	VLAN 80	192.168.80.0/24
Store	VLAN 70	192.168.70.0/24
Logistics	VLAN 60	192.168.60.0/24

### 2nd Floor

Department	VLAN ID	Network
Finance	VLAN 50	192.168.5.0/24
HR	VLAN 40	192.168.4.0/24
Sales/Marketing	VLAN 30	192.168.3.0/24

### 3rd Floor

Department	VLAN ID	Network
Admin	VLAN 20	192.168.2.0/24
IT	VLAN 10	192.168.1.0/24

## 6. Routing Protocol
- Use OSPF (Open Shortest Path First) as the dynamic routing protocol.
- OSPF should advertise all VLAN networks across routers.
## 7. DHCP Configuration
- Each router must be configured as a DHCP server.
- All devices should obtain IP addresses automatically.
## 8. Network Communication
All devices across all VLANs and floors must be able to communicate with each other.
## 9. Remote Access (SSH)
- Configure SSH (Secure Shell) on all routers.
- Enable secure remote login access.
## 10. Test PC (IT Department)
- Add a Test PC in the IT department.
- Connect it to FastEthernet 0/1 (Fa0/1).
- Use this PC to:
  - Test SSH connectivity
  - Verify remote access
## 11. Port Security Configuration
- Configure Port Security on the IT department switch.
- Apply the following settings on Fa0/1:
  - Allow only Test PC
  - Use sticky MAC address
  - Maximum MAC addresses: 1
  - Violation mode: shutdown
## Expected Outcome
After implementation:
- VLANs are properly configured
- Inter-VLAN routing is functional
- OSPF routing is working correctly
- Devices receive IP via DHCP
- Wireless connectivity is available
- Printers are operational
- SSH remote access is secured
- Port security restricts unauthorized access
- Full communication across all floors is achieved